## Slide 1: Properties, Handling and Mixing of Particulate Solids
By
Sidra Jabeen
Department of Chemical Engineering,
University of Engineering & Technology Lahore

## Slide 2
Particle Size
Some particles conform to standard configuration like;
  Spherical
  Cylindrical
  Cubical
Some do not conform to any of these standard configurations Irregular shape particles

## Slide 3
Particle Size
Feret’s Diameter
Martin’s Diameter
Projected area Diameter

## Slide 4
Particle Size
Latest system of defining particle size is by comparison with standard configuration (sphere)  That is called the equivalent size / equivalent diameter or Equivalent Spherical Diameter (ESD) of irregular particle defined as:
The size of the spherical particle having the same controlling characteristics as the particle under consideration.

## Slide 5
Particle Size in terms of controlling characteristics
For defining the size of catalyst particle, surface area is chosen as controlling characteristics.
Surface diameter: Diameter of the spherical particle having the same surface area as the particle.

## Slide 6
Particle Size in terms of controlling characteristics
Settling velocity of particle in a liquid is very much controlled by the volume of the particle.
Volumetric diameter: Diameter of the spherical particle having the same volume as the particle under consideration.

## Slide 7
Particle Size in terms of controlling characteristics
Motion of liquid drops in a gas depend not only on liquid drop volume but also at interfacial tension at the gas-liquid interface. Both the volume and surface area of liquid drop are controlling parameters here.
Volume Surface diameter: Diameter of the spherical particle having the same volume per unit surface area as the liquid drop under consideration.

## Slide 8
Sphericity
Sphericity is a measure of roundness of a shape of particle.
Sphericity is defined for a non-spherical particle
Dimensionless quantity
Sphericity is s/v ratio for a sphere of diameter Dp divided by s/v ratio of particle whose nominal size is Dp.

## Slide 9
To equate some property of the irregular shaped particle to a sphere with the same property, e.g. same volume as particle:
Sphericity
Has the same volume as a sphere

## Slide 10
Sphere

## Slide 11
Ideal Cylinder

## Slide 12
Long Cylinder

## Slide 13
Cube

## Slide 14
Sphericity of various particle shapes

## Slide 15
Measurement of Particle size (Regular)

## Slide 17
Units used for particle size depend on the size of particles:
Coarse particles: inches or millimetres
Fine particles: screen size
Very fine particles: micrometers or nanometers
Ultra fine particles: surface area per unit mass, m2/g

## Slide 18
Particle Size Analysis Methods
1. Visual methods (e.g., optical, electron, and electron microscopy and image analysis)
2. Separation methods (e.g., sieving, classification, impaction, electrostatic differential mobility)
3. Scanning methods (e.g., electrical resistance zone, laser diffraction)
4. Surface methods (e.g., permeability, adsorption)